## Slide 1: 1. Cut Steel
Tubes, 2 ea: 1/4” x 6” x 12” x 26” long
Angle iron, 10 ea: 27” per frame diagram
Angle iron 1/4” x 2” x 2”, 2 ea: 4”, 1 ea: 2”, 2 ea: 8”
Flat steel, 1/4” x 6”: 1 ea: 6”, 4 ea: 12”
Flat steel, 1/4” x 8”: 13.5”
Flat steel 1/8” x 4”: 1 ea: 14”, 2 ea: 1”
1 ½" x 2” pipe coupling: cut in half
1” engine shaft: cut in half
3/4” 11 tooth spline shaft: cut in half

## Slide 2: 2. Fabricate tanks
Torch, then grind tubes and end plates
Drill ½” holes for sight gauge
Install sight gauge
Weld flanges, pipe coupling and filler neck
Weld end plates on tanks
Weld supports for engine & control panel
Weld battery bracket to fuel tank and solenoid bracket to battery bracket
Soap bubble test and re-weld if necessary
Drill smaller 7/16” holes & tap ¼” NPTF
Mask holes and paint

## Slide 3: 3. Shaft Coupling
Cut couplings in half
Preferably: Use lathe to turn down cut ends
Insert plug into coupling halves
Clamp and weld
Let cool standing vertically
Paint external surfaces

## Slide 4: 4. Weld Frame
Note: Mitered joints welded on inside and outside
Begin in one corner, lay two members on flat surface, clamp and weld
Add third member, clamp and measure – verify parallel with opposing member and weld
Add forth member, verify alignment and weld
Complete second rectangle
Weld hoist points to upper frame members
Align fifth and sixth members on one rectangle and weld
Align second rectangle to first, position tanks inside frame and complete frame welds
Weld expanded steel to hydraulic reservoir
Weld solenoid bracket to battery bracket
Paint frame & tank surfaces that will be inaccessible later
Weld tanks to frame

## Slide 5: 5. Engine/pump mount
Torch & drill holes in engine & pump plates – verify that holes on engine plate match those on support brackets on tanks
Weld angle iron to pump plate
Mount pump on pump plate
Mount engine on engine plate
Insert key in shaft coupling and connect to engine
Slide pump assembly to shaft coupling
Place 4” spacers between pump & engine plates
Tack angle iron to engine plate
Remove spacers and weld
Remove engine / pump assembly and paint

## Slide 6: 6. Fabricate Control Panel
Torch, drill, file control panel holes to drawing
For key switch hole, use switch while filing to test for proper hole size
Weld throttle bracket to back side & drill bracket
Paint
Mount control panel components:
  Quick couplers
  Key switch
  Throttle

## Slide 7: 7. Fabricate Wire Harness
Cut wire:
  2 ea: 10” 2 ga red
  1 ea: 12” 2 ga black
3/8” copper tubing: 6 ea @ 1 ½”
Align wires, cut and strip ends appropriately
Crimp fan connectors on wires
Crimp circular lug on wire for solenoid
Crimp pins on wires and insert into connector
On large gauge wires, begin on ends with single wire – flare ends of copper tubing, insert wire, flatten with hammer and drill
Proceed to ends with multiple wires – flare, insert, flatten and drill
Cut heat shrink tubing, install on cables with multiple wires and heat to shrink

## Slide 8: 8. Oil Cooler & Fan
Put teflon tape onto elbow connector NPT threads
Screw elbows into oil cooler
Position oil cooler: elbows up and facing you
Insert plastic brackets in fan
Place fan on oil cooler – wires pointing left
Insert plastic fasteners through oil cooler and plastic fasteners, then secure (use foam pads to protect fins)

## Slide 9: 9. Install Engine / Pump
Hoist engine / pump
Attach vibration isolators to supports on tanks – loosely tighten from underneath
Lower engine into frame until mated with isolators
With full weight on vibration isolators install and tighten nuts

## Slide 10: 10. Install Oil Cooler & Fan
Slide oil cooler / fan in place – be careful not to damage cooler fins
Loosely connect hydraulic hoses to oil cooler elbows
Test alignment of hydraulic hoses and adjust elbows if necessary
Install oil cooler/fan to expanded steel using rubber bushings and bolts

## Slide 11: 11. Install Control Panel
Position control panel
Connect and tighten hydraulic hoses between oil cooler and control panel
Connect ¼” hose for “Tank Return” to control panel and tank using hose clamps

## Slide 12: 12. Wire Harness and Battery
Mount solenoid to bracket
Insert battery in place
Plug key switch connector to switch
Plug in fan connectors
Connect wire lug to solenoid
Connect black battery cable to engine bolt and to battery
Connect red cable to solenoid and engine
Connect red cable to solenoid, then battery

## Slide 13: 13. Install Suction Plumbing
Use teflon tape on all NTP threads!
Install tank strainer in tank
Install 1” x 4” nipple in strainer
Install 1” elbow on nipple
Install suction hose with 2 ea hose clamps

## Slide 14: 14. Install Supply Plumbing
Use Teflon tape on all NPT threads!
Connect “long” elbow to pump
Connect ½” 1' hose between pump elbow and quick connect on control panel – minimize stress on hose
Install ¾” nipple and filter head to tank – make sure fluid flow is into tank
Install ¾” elbow in filter head
Install filter on filter head
Connect and tighten all ¾” JIC fittings

## Slide 15: 15. Fill With Fluids

## Slide 16: 16.Test